## Slide 1: Out-of-order execution: Load-Store architecture
Igor Smirnov
22/03/2019

## Slide 2: Refresher: Data Flow Execution
(1) r1  r4 / r7
(2) r8  r1 + r2
(3) r5  r5 + 1
(4) r6  r6 – r3
(5) r4  load [r5 + r6]
(6) r7  r8 * r4
In-order execution
Out-of-order execution
1
3
4
2
5
6
r1
r5
r6
r4
r8
Example:
Data Flow Graph
1
3
4
2
6
5
3
4
6
5
1
2

## Slide 3: Memory Dependencies
OOO engine can track dependency through registers, but not through memory
    (1) Mem[r1]  …
    …
    (6) …  Mem[r1]
Unlike register dependencies, memory dependency cannot be known at allocation
    (1) Mem[r2]  …
    …
    (6) …  Mem[r3]
  If instruction(6) will executes before (1), it will read a wrong value from memory
  Registers r2 and r3 may have the same values

## Slide 4: Why use memory?
In the beginning registers were expensive
  Only few were accessible: 8 in x86, 31 in MIPS
Now CPU can handle hundreds of registers via RAT
  Why not access them directly on ISA-level?
  If compatibility is an issue, why brand new RISC-V has only 31 registers?
Notes: Context switch save/restore overhead with increased number of arch registers (must be saved/restore at every switch)
More bits in instruction encoding for registers enumeration
Register renamer (RAT) is already good at handling this

## Slide 5: Store Execution
Stores are never performed speculatively
  There is no transparent way to undo them
Stores are also never re-ordered among themselves
  The store is dispatched only when
    its address is ready
    its data is ready
    there are no older stores awaiting dispatch
Store commits its value to cache post retirement
(1) r1  r4 / r7
(2) r8  r1 + r2
(3) r5  r5 + 1
(4) r6  r6 – r3
(5) [r5 + r6]  store r4
(6) r7  r8 * r4

## Slide 6: Load Execution
Decision: load should wait until all the previous stores write into the memory (cache)
It works, but it is too slow — stores write after retirement
If we leave only the real dependencies between store and load, we can wait only for the specific store
    Mem[r1]  …
    Mem[r2]  …
    …
    (6) …  Mem[r1]

## Slide 7: Load and Store Buffer
Improvement: load does not wait if there is no intersection
  Need to wait until all previous stores calculate their address
  Then, check for intersection
  no intersection → load waits nothing
  intersection → we have a real data dependency, wait for that store
Store can be at any ROB entry → any entry should be checkable
  Too large and slow HW
  On the other hand, not every instruction is load or store
  Like SQ, we can use smaller buffers for stores and loads only (store buffer or SB and load buffer or LB)
  All complex check of the address are done in LB and SB
  ROB just keeps the order of instructions

## Slide 8: Store Forwarding
Load waits only for the specific store, and store waits for:
  its address
  its data
  its program order
For loads, there is no need to maintain the program order.
Improvement: load can take data of the producing store bypassing cache, it is called Store Forwarding

## Slide 9: Intersection ≠ Forwarding
Forwarding condition is stronger than simple intersection
Example:
  sb $r1, 0x0($r3) // store byte
  sb $r2, 0x2($r3) // store byte
  lw $r4, 0x0($r3) // load FOUR bytes
Forwards (1)→(3) and (2)→(3) are not possible
However, (3) must wait for retirement of (2)
Can we forward from two stores? Theoretically, yes, but such programs are too rare to justify complexity

## Slide 10: SB and LB Operation
(5) …  Mem[r5]
(4) Mem[r4]  …
 | Address | Previous store | Waiting store | Ready?
0 |  |  |  | 
1 |  |  |  | 
2 |  |  |  | 
3 |  |  |  | 
4 |  |  |  | 
5 |  |  |  | 
… |  |  |  | 
M |  |  |  | 
(3) …  Mem[r3]
(2) Mem[r2]  …
(1) Mem[r1]  …
 | Address
0 | 
1 | 
2 | 
3 | 
… | 
N | 
Store Buffer
…
…
(1) Mem[r1]  …
(2) Mem[r2]  …
(3) …  Mem[r3]
(4) Mem[r4]  …
(5) …  Mem[r5]
Example:
(1)
(2)
(4)
(3)
(5)
NA
NA
NA
NA
1
no
NA
Load Buffer
1
2
no
2
oldest unknown
address: [0x35]
address: [0x01]
address: [0x25]
address: [0x25]
address: [0x35]
[0x25]
[0x01]
[0x25]
[0x35]
[0x35]
[0x25]
OK
yes
[0x35]
NO: (1)
0

## Slide 11: Summary
For each load, three cases are possible:
  No dependency from store — execute as soon as possible
  Forwardable dependency from store — take data from that store
  Non-forwardable dependency from store — wait for the cache update (rarely)

## Slide 12: False Dependency from Store Data
Data is not required to check that store and load have no dependency
Address is calculated when store is executed
But, store is sent to execution only all its sources (including data) are ready → there is a false dependency from data
(1) r1  …
(2) r2  …
(3) Mem[r1]  r2
…
(N) …  Mem[r3]
1
2
3
N
r1
r2
address
Example:
Data Flow Graph
  r3 != r1 → (3) and (N) are not overlapped
  False dependency:
  in fact, (N) does not need to wait (2)

## Slide 13: STA and STD
To remove false dependency in case of absence of overlapping store instruction is executed in two steps:
  Store address calculation (STA)
  Store data calculation (STD)
Load is waiting for STD only if it overlapped with STA
(1) r1  …
(2) r2  …
(3) addr  [r1]
(3’) Mem[addr]  r2
…
(N) …  Mem[r3]
1
3
N
r1
addr
Example:
Data Flow Graph
  Exists only if overlapping is detected
STA →
STD →
2
r2
3’
data

## Slide 14: SB and LB Operation: STA and STD
(5) …  Mem[r5]
(4) Mem[r4]  …
 | Address | Previous store | Waiting store | Ready?
0 |  |  |  | 
1 |  |  |  | 
2 |  |  |  | 
3 |  |  |  | 
4 |  |  |  | 
5 |  |  |  | 
… |  |  |  | 
M |  |  |  | 
(3) …  Mem[r3]
(2) Mem[r2]  …
(1) Mem[r1]  …
 | Address
0 | 
1 | 
2 | 
3 | 
… | 
N | 
Store Buffer
…
…
(1) Mem[r1]  …
(2) Mem[r2]  …
(3) …  Mem[r3]
(4) Mem[r4]  …
(5) …  Mem[r5]
Example:
(1)
(2)
(4)
(3)
(5)
NA
NA
NA
NA
1
no
NA
Load Buffer
1
2
no
2
oldest unknown
address: [0x35]
address: [0x01]
address: [0x25]
address: [0x25]
address: [0x35]
[0x25]
[0x01]
[0x25]
[0x35]
[0x35]
[0x25]
yes
[0x35]
0
Data
data: 0x100
0x100
(1)
yes
hit

## Slide 15: Load speculation
For correctness, load has to wait all older STAs
But we can already speculate on branches — why not speculate on store-load dependencies?
The idea is not to wait for all older STAs, but execute speculatively
  As soon as STAs are ready, verify our speculations

## Slide 16: SB and LB Operation: speculation
(5) r6  Mem[r5]
(4) Mem[r4]  …
 | Address | Previous store | Waiting store | Ready? | OK?
0 |  |  |  |  | 
1 |  |  |  |  | 
2 |  |  |  |  | 
3 |  |  |  |  | 
4 |  |  |  |  | 
5 |  |  |  |  | 
… |  |  |  |  | 
M |  |  |  |  | 
(3) …  Mem[r3]
(2) Mem[r2]  …
(1) Mem[r1]  …
 | Address
0 | 
1 | 
2 | 
3 | 
… | 
N | 
Store Buffer
…
…
(1) Mem[r1]  …
(2) Mem[r2]  …
(3) …  Mem[r3]
(4) Mem[r4]  …
Example:
(1)
(2)
(4)
(3)
(5)
NA
NA
NA
NA
1
no
NA
Load Buffer
1
2
no
2
address: [0x35]
address: [0x01]
address: [0x25]
address: [0x25]
address: [0x35]
[0x01]
[0x25]
[0x35]
[0x25]
yes
[0x35]
Data
yes
(6) r7  r6 + r8
yes
hit

## Slide 17: Speculation prediction
Speculation requires decision making
The idea is to track history similar to branch prediction
Approach 1:
  assume “unknown” loads as speculative
  if the assumption is wrong, add PC of load to “blacklist”
  big overhead on rollbacks
Approach 2:
  assume “unknown” loads as non-speculative
  if there were no STAs to wait, add PC of load to “whitelist”
  moderate overhead as loads wait STAs in the beginning

## Slide 18: Summary
Stores write data in-order after retirement
Loads read data
  from cache, if they do not depend on non-retired stores
  from SB, if store forwarding is possible
  speculatively from cache/SB with mandatory checks
LB and SB track dependencies between loads and stores
LB and SB are responsible for performing 3 actions:
  Blocking loads dependent on stores
  Forwarding data from stores to loads
  Checking correction of load speculation

## Slide 19: Thank You