## Slide 1: Simultaneous Multithreading
Oleg Ladin
12/04/2019

## Slide 2: Refresher: Motivation
Increasing ST performance becomes harder and less power efficient
Area budget can be divided in several ways:
  Single core 6x area, 2.9 performance boost
  3 smaller cores 2x area, 2.0 performance boost each 6x area, 6.0 performance boost total!

## Slide 3: Why ST performance doesn’t increase?
Most applications’ sustained throughput << the peak IPC
  No ILP can be extracted → CPU resources are not used
  Pipeline stall (e.g. cache miss) prevents forward execution
What is the solution? The solution is to run 2nd application on the same resources
  CPU resources are utilized
  Stalls are hidden by other thread processing
Ok, where can one find the 2nd application?
Schedule queue entries
1
2
3
4
5
6
Data Flow Graph
0
0
1
2
3
4
5
6
EXE
EXE
EXE
EXE
3
1
2
0
2nd application
0
1
0
1
2
3
4
5
6
2
3

## Slide 4: Refresher: Thread-level parallelism
To achieve the best performance, workload should be parallelized to several threads
This is possible due to the thread-level parallelism (TLP)
  Unlike ILP, TLP is extracted manually by programmer
Threads can be extracted either from:
  The same application
  Different applications running simultaneously
  Operating system services
Previously each thread was executed on separate single core
  Now assume each core could handle more than one thread execution
  CPU supports ST and MT execution modes

## Slide 5: Simultaneous Multithreading
Physically we have the same amount of cores
Logically there are twice more cores
  OS schedules tasks on logical CPUs
Each logical processor maintains its own arch state
  Complete set of architectural registers (General-purpose registers, Control registers, Machine state registers, Debug registers)
  Instruction pointers
Each logical processor has its own interrupt controller
CPU
Core 1
Core 2
Cache
Memory

## Slide 6: Resource Sharing
Each pipe-stage is occupied by one of the threads
Resources are either replicated, partitioned or shared
Replicated resources are ones which are vital to maintain two fully independent contexts on each logical processor
  Main source of HW size growth
Partitioned resources are mostly queues that decouple pipeline stages
  Could be unified in ST execution mode
Shared resources are ones which don’t care about threading at all
Arch State
Physical Registers
Arch State
APIC
Fetch
Decode
Queue
Queue
Rename & Allocate
OOO Scheduler / Execute
ROB
ROB
Retirement
Queue
Queue
PC
PC
APIC
SQ

## Slide 7: Example: Branch Predictor sharing
BP operates in terms of virtual addresses and has shared structure in MT mode
To avoid potential aliasing problems in case of virtual address overlapping BP entries could be marked with thread ID

## Slide 8: Example: Schedule queue sharing
In MT mode schedule queue is dynamically partitioned
Each thread has its own small number of SQ entries
  This prevents one thread monopolize whole machine resources
  Each thread has ability for forward execution
Remained entries could be allocated by any thread
Schedule queue entries

## Slide 9: Example: ROB replication
In MT mode ROB is partitioned, each part contains instructions only from one thread
  Provide fairness execution of each thread
  It’s complicated to make sharing scheme with dynamic repartitioning
Each thread has its own retirement logic
  Stall in one thread doesn’t block retirement of another thread
In case of mispredictions, only instructions from affected thread are cleared
Retirement point (thread 1)
Retirement point (thread 2)

## Slide 10: Example: Data cache sharing
Caches are addressed in physical addresses and considered as shared
  If the data is common (cooperative workload), both threads hit to cache
  Otherwise, LRU algorithm works
  Ambiguity is avoided: physical address is thread-independent

## Slide 11: Resource sharing: pipeline overview
Overhead on HW size mostly comes from replicated resources
  2x ARF, 2x PC, 2x APIC
  Additional HW for thread switching between pipeline stages (thread selectors)
Still overhead is much less than 2x core

## Slide 12: SMT pros and cons
Pros:
  Increases overall system’s throughput by utilizing machine resources more effectively
  Shadow pipeline hazards and allocation stalls
  Introduce little addition HW (only replicated resources)
Cons:
  ST performance of each thread is smaller
  Could significantly drop performance due to cache thrashing
  Unlikely help traces with enough ILP or high memory bandwidth

## Slide 13: Implementations
SMT technology been around 1950s
  First researched by IBM in ACS-360 project (1968)
  Dean M. Tullsen et al – Simultaneous Multithreading: Maximizing On-Chip Parallelism – University of Washington (1995)
  Major commercial CPU – DEC Alpha 21464 w/ SMT4 (cancelled 2001)
  Intel Pentium 4 / Xeon – SMT2 support in NetBurst architecture (2002)
Modern implementations:
  2 threads: Intel Atom/Core i7/Xeon (since 2008), AMD Ryzen, IBM Power 6
  4 threads: Intel Xeon Phi, IBM Power 7 (8 cores - 32 threads)
  8 threads: IBM Power 8/9 (12 cores – 96 threads)

## Slide 14: Thank You

## Slide 15: Backup section